## Slide 1: Advanced Computer Network (4350706) Unit-3 Unicast Routing
Prepared By :
Mr. Chetan C. Kamani
Lecturer, Computer Engineering Department
Government Polytechnic, Jamnagar

## Slide 2: Topics to be discussed
Introduction
Optimization
Intra and Interdomain routing protocol.

## Slide 3: Introduction
A routing table can be either static or dynamic.
A static table is one with manual entries.
A dynamic table, on the other hand is one that is updated automatically when there is a change somewhere in the internet.
Today, an internet needs dynamic routing dynamic routing tables.
The tables need to be updated when a router is down, and they need to be updated whenever a better route has been found.
Routing protocols have been created in response to the demand for dynamic routing tables.

## Slide 4: Introduction
A routing protocol is a combination of rules and procedures that lets routers in the internet inform each other of changes.
It allows routers to share whatever they know about the internet or their neighborhood.
The sharing of information allows a router in San Francisco to know about the failure of network in Texas.
The routing protocols also include procedures for combining information received from other routers.

## Slide 5: Optimization
A router receives a packet from a network and passes it to another network.
A router usually attached to several networks.
When it receives a packet, to which network should it pass the packet? The decision is based on optimization: Which of the available pathways is optimum pathway? What is the definition of the term optimum?
One approach is to assign a cost for passing through a network. We call this cost a metric.

## Slide 6: Optimization
However, the metric assigned to each network depends on the type of protocol.
Some simple protocols, such as Routing Information Protocol (RIP), treat all network as equals. The cost of passing through a network is the same; it is one hop count. So if a packet passes through 10 networks to reach the destination, the total cost is 10 hop counts.
Other protocols, such as Open shortest path first(OSPF), allow the administrator to assign a cost for passing through a network based on the type of service required. A route through a network can have different costs(metrics).
Other protocols define the metric in a totally different way. In the Border Gateway Protocol (BGP), the criterion is the policy, which can be set by administrator. The policy define what paths should be chosen.

## Slide 7: Intra- and Interdomain Routing

## Slide 8: Questions

## Slide 9: References
Data Communication and Networking, Fifth Edition, BEHROUZ A. FOROUZAN
Data Communication and Networking, Fourth Edition, BEHROUZAN A. FOROUZA
https://www.geeksforgeeks.org/introduction-of-classful-ip-addressing/

## Slide 10
Thank You